Make sure robot is physically near the starting position
Make sure the emergency stop is depressed so that Roberto doesn't run away.

Open a terminal (ctrl-alt-t)

Change directories (you can pres tab to autocomplete this)
$ roscd cwru_tour_guide

Run the tour software (again, you can press tab to autocomplete)
$ ./roberto_bk_nav_launch.sh

A window called “rviz” should come up. If it doesn't, press ctrl-c in the terminal to quit, and try to run it again.

If the robot appears to be in the wrong position, click on “2D Pose Estimate” in rviz, and click on where the robot actually is within the map. Drag to set orientation.

Left: “rviz” window showing robot with incorrect localization
Middle: giving the robot its correct pose
Right” Robot with correct localization (blue laser pings align with map)

After ensuring that the robot knows correctly where it is, release the emergency stop. The robot should automatically move.

If the robot seems to get stuck, a new goal can be given manually. In rviz, click on “2D Nav Goal” and click where on the map you want the robot to go. Only goals within 5m are allowed. The tour script will automatically resume when the robot is within 1m of its originally-intended goal.

Sometimes, the robot may get stuck with an obstacle at close range. In this case, depress the emergency stop and manually pull the robot backward about a foot. Ensure that the robot's localization is good, and release the emergency stop. A new goal may need to be given manually.

Sometimes, it may be desirable to run the tour without the script for troubleshooting. In this case, edit the file ~/dev/cwru-ros-pkg/cwru_tour_guide/tour_guide_executive/start_executive.launch and set the parameter “skip_sounds” to “true”.