Introduction to Point-Cloud Processing
Wyatt Newman
March, 2015

Introduction: Three-D sensing is increasingly common in robotics. Example sources of 3-D data include tilting or rotating LIDARs, stereo cameras, or structured-light processing, such as the Microsoft Kinect sensor. Each of these sensors has its own virtues and limitations. Rotating LIDAR instruments can require a relatively long acquisition time to achieve reasonable 3-D sampling. The resulting 3-D images can be fairly noisy (on the order of cm, for the Hokuyo). However, such sensors have good range and work outdoors. Stereo vision can be relatively inexpensive, can be high resolution, and can augment range information with color and intensity. However, the range and field of view are restrictive, relative to LIDARs. Further, stereo vision depends on viewing targets that have suitable “texture”, which helps to address the left/right camera pixel correspondence problem for generating disparity maps. The useful range of stereo vision depends on the interocular distance; wider separation between the cameras is required for greater depth range, but this also limits the near range (i.e., making the system far-sighted). On the other hand, optics can be designed over huge variations—from telescopes to microscopes.

The Kinect sensor uses a structured-light source of infra-red, projecting a “speckle” pattern. A single camera detects this projected pattern and interprets range from triangulation, equivalently deducing the shape of illuminated scenes from how the speckle pattern is projected over surfaces. The Kinect camera has surprisingly good performance for its low price. The depth points are “colorized” by associating corresponding data from a 2nd (color) camera. The density of points is high. However, the field of view and the range are limited (optimized for gaming applications), and this device does not work in sunlight.

This document will focus on use of the Kinect sensor and interactions with Rviz, but the principles are applicable to 3D images from other sources.

Point Clouds: There are a variety of representations of 3-D images. Many variations are accommodated with the “PointCloud” definition. (see http://pointclouds.org/about/).

A point-cloud has a header, with fields for a time stamp and for a reference frame. A point-cloud also has fields for “height,” “width,” and “is_dense.”

One style of representation is to merely list “points” in a random order, where each point has associated data. This is an “unordered” point cloud. Unordered point clouds have a “height” of 1, and a “width” equal to the number of points. Data that originates from a rotating LIDAR typically results in unordered point clouds, since this data is not acquired in a simple raster pattern. Alternatively, stereo cameras and the Kinect camera produce “ordered” point clouds. Points in an ordered point cloud can be accessed by row and column (though index computations are required). The row and column indices of the point-cloud structure correspond to row and column indices of the image plane. At each such [i][j] location, one may find N-dimensional data, e.g. (x,y,z,R,G,B). In contrast to an unordered point cloid, an ordered point cloud can offer computational efficiencies, since points that are close together in [i][j] space are (typically) close together in (x,y,z,R,G,B) space—at least when these points correspond to samples on a smooth patch of surface in the scene.

The “is_dense” field of a point cloud declares whether or not (true/false) every point in the point cloud has valid data. Commonly, sensors provide imperfect results. Stereo vision, for example, typically suffers from inability to resolve the correspondence problem where there is insufficient texture in the scene, and corresponding points lack computable depth. Coordinates for such points may containt “inf” or “NaN” to indicate they are not valid. Such points may be included in the point-cloud so as to preserve order in an ordered point cloud, or they may be included in a stream if the sensor is not smart or fast enough to remove such points. If the point cloud is not “dense”, your processing code must test each value for validity.

A point-cloud may be constructed from a single view (e.g., from a robot standing still, staring at a scene). Alternatively a point-cloud may be the result of multiple sensing devices (but with all points transformed to a common reference frame), or possibly from a single sensor moving around in the environment (but, again, with each sensor-data contribution transformed into a common reference frame). If it is known that a range image is acquired from a single viewpoint, this information can be used to help reduce confusion in perceptual processing from occlusions and shadowing.

Point-cloud processing can be demanding of required memory, computation time and bandwidth. A 640x480 image from a Kinect sensor provides over 300k points, each with (x,y,z,R,G,B). Updated at 30Hz, this consumes approximately 300MB/sec of communication bandwidth (transmitting point clouds as ROS messages). Mere seconds of “bagging” such data can rapidly fill files on the order of gigabytes.

Because point-cloud processing can be demanding, it is important that algorithms analyzing point clouds are particularly efficient. Algorithms within the “Point Cloud Library” (PCL; see http://pointclouds.org) are optimized for efficiency in C++ code. Further, some of the core routines exploit Intel's Streaming SIMD Extensions (SSE), and some of the algorithms exploit multi-core CPU capabilities. Some of the internal computations use the “Eigen” library (see http://eigen.tuxfamily.org), which performs linear-algebra computations efficiently.

Tutorials on how to use the “Point Cloud Library” can be found at: http://pointclouds.org/documentation/tutorials/. Methods within this library are available for a useful variety of point-cloud processing, and all of the source code is openly available.

Since point clouds can be large, it is important to avoid making copies of these. Instead, point clouds are passed to functions via pointers. This provides a significant speed-up, but at the cost of some confusion regarding pointers and pointer dereferencing. It can be helpful to emulate working examples to construct new point-cloud processing code.

Xxx
*rviz publish points
*subscribing to pointclouds
*publishing pointclouds
*computing a centroid—manually
*outlier removal
*computing a surface normal (find the code: http://pointclouds.org/documentation/tutorials/normal_estimation.php
*transforming data (R'*points)
*filtering data (z_eps; indices)
*identifying planes (RANSAC vs selected-point assistance)
*NEXT: find points of a Coke can (problem set?)